## Slide 1: Bridging the Gap between Software and Hardware Techniques for I/O Virtualization
Jose Renato Santos, Yoshio Turner, G.(John) Janakiraman, Ian Pratt
USENIX 2008

## Slide 2: Introduction
I/O virtualization degrades performance
Each guest-device interaction requires interception, validation, and handling
Especially in high-bandwidth NICs
  Every packet would need to be inspected by virtualization layer

## Slide 3: Paravirtualization
Guest executes a paravirtualized (PV) driver
  Simplified abstract device model
Actual driver resides in the hypervisor or driver domain
Device driver domain
  Privileged access to the I/O hardware

## Slide 4: Device Passthrough
https://wiki.xen.org/images/1/17/Device_passthrough_xen.pdf

## Slide 5: Device Driver Domain
Advantages
  Legacy OS devices for portability
  Safe execution environment
  Isolation
Drawbacks
  CPU overhead -> up to 4X slower!
  Progress made on transmit path but not receive path

## Slide 6: Direct I/O
Device presents multiple logical interfaces
  Securely accessed by VMs
  Virtualization layer bypassed
  Near native performance
Drawbacks
  HW support needed
  Isolation and safety from buggy drivers compromised
  No live migration
  VMM must include many device drivers

## Slide 7: Xen Driver Architecture
Notes: Netfront is the driver guest interacts with
Interrupts handled by hypervisor
Notifies appropriate driver domain via virtual interrupts
Shared memory channel b/w netfront and netback
SW Bridge: routes packets b/w physical device & multiple guests through their netback interfaces

## Slide 8: I/O Channels
Event notification mechanism
Bidirectional ring of async requests
  netfront => requests => netback
  netfront <= responses <= netback
  Virtual interrupts indicate new requests/responses posted

## Slide 9: Page Grants
Page grants allow driver domains to access I/O buffers in guest memory
Guest sends I/O buffer descriptors with requests to netback including guest address and callback function

## Slide 10: Transmission (TX)
DomD makes hypercall mapping guest page into its address space before sending through the bridge
Physical driver fills the buffer and frees the page
Callback function invoked sending data back to netfront
Page grant revoked

## Slide 11: Receive (RX)
netfront posts page grants to the RX I/O channel
netback receives packet from the bridge and retrieves a grant
Grant copy hypercall transfers packet to guest page
netback sends response to guest notifying of new packet
netfront reads packet and revokes grant

## Slide 12: Network Performance Analysis
Three Models
  Xen PV Driver
  Xen Direct I/O
  Native Linux
Domains
  Dom0 == DomD
  DomU == guest
Notes: Uses netperf UDP_STREAM microbenchmark
  Difficult to quantify CPU costs for TCP due to ACK packets

## Slide 13: Network Performance Analysis
Uses netperf UDP_STREAM microbenchmark
  Difficult to quantify CPU costs for TCP due to ACK packets
IOMMU prevents guests from accessing
each others’ memory via DMA
Direct I/O results optimistic due to lack of IOMMU overhead
  Authors unable to obtain one…

## Slide 14: Network Performance Analysis
  app: user-space application on guest
  usercopy: packet copy to user app
  kernel: kernel-space code on guest
  xen: hypervisor code related to guest
  grantcopy: driver to guest data copy
  kernel0: kernel code in driver domain
  xen0: hypervisor code in driver domain

## Slide 15: Network Performance Analysis
Direct I/O Analysis
  31% overhead w.r.t. native Linux on RX
  Mostly in the DMA interface
  DMA driver must translate virtual addresses to device bus addresses
  Requires SW emulated TLB code on x86
  Linux bounce buffer if physical memory not contiguous
Notes: Uses netperf UDP_STREAM microbenchmark
  Difficult to quantify CPU costs for TCP due to ACK packets

## Slide 16: Network Performance Analysis

## Slide 17: Network Performance Analysis
PV Driver: Copy overhead
  x86 faster when memory addresses have same 64-bit word alignment, fastest if cache line aligned
  Network packets are non aligned due to 14B Ethernet header
Notes: Uses netperf UDP_STREAM microbenchmark
  Difficult to quantify CPU costs for TCP due to ACK packets

## Slide 18: Network Performance Analysis
PV Driver: Kernel overhead
  ↑ CPU cycles due to fragments in guest socket buffers
  TCP Segmentation Offloading (TSO) and Large Receive Offloading (LRO) enable large packets spanning many pages
  Fragmentation introduces copy and socket buffer allocation overheads
Notes: Uses netperf UDP_STREAM microbenchmark
  Difficult to quantify CPU costs for TCP due to ACK packets

## Slide 19: Network Performance Analysis
PV Driver: Kernel overhead
Notes: Uses netperf UDP_STREAM microbenchmark
  Difficult to quantify CPU costs for TCP due to ACK packets

## Slide 20: Network Performance Analysis
PV Driver: Hypervisor overhead
  ↑ CPU cycles due to code executing in the driver domain
  Mostly page grant operations and scheduling
  With DomD and guest on different cores, accessing schedule data structures results in more cache misses
  Grant operation costs from spin locks, page pinning, and atomic swap operations
  Can be optimized by moving driver domain operations into guest
Notes: Uses netperf UDP_STREAM microbenchmark
  Difficult to quantify CPU costs for TCP due to ACK packets

## Slide 21: Network Performance Analysis
PV Driver: Hypervisor overhead
Notes: Uses netperf UDP_STREAM microbenchmark
  Difficult to quantify CPU costs for TCP due to ACK packets

## Slide 22: Network Performance Analysis
PV Driver: Driver domain overhead
  Mostly caused by bridge and netfilter functions
  Can be disabled if kernel is configured properly
Notes: Uses netperf UDP_STREAM microbenchmark
  Difficult to quantify CPU costs for TCP due to ACK packets

## Slide 23: Xen Network Design Changes
Architecture-independent optimizations
  Disable netfilter bridge
  Aligned data copies
  Avoiding socket buffer fragments
  Page grant optimizations

## Slide 24: Xen Network Design Changes
Data copying moved to guest
  Additional copy between DomD and guest is overhead not required in native Linux
  The data copy is likely performed by different CPU cores (one for driver domain, one for guest) leading to poor cache locality
  Ownership of the page in the driver domain containing the packet from the NIC is transferred to the guest

## Slide 25: Xen Network Design Changes
Data copying moved to guest
  Grant copy operation is performed on the guest just like the second data copy so the page is likely to exist in L2 cache
  Avoids polluting DomD CPU cache
  Improved scalability for multiple guests (avoids DomD bottleneck)
  Enables other optimizations (e.g., socket buffer fragment allocation)
Saves ~2250 cycles or 276% of native

## Slide 26: Xen Network Design Changes
Grant mechanism extensions
  DomD issues grant to the guest
  Packets received from other guests are not owned by driver domain
  Requires grant transitivity, guest domain can transfer grant to another
  Same I/O buffer can receive data from different guests => potential security violation
  Grants extended with offset and size fields so receiving guest only receives access to memory containing received packet data

## Slide 27: Xen Network Design Changes
Multi-queue device support
  Moving extra data copy to guest is good, eliminating it better!
  If only NIC could place packets directly into guest kernel buffer
  Driver domain is bypassed
  Some NICs demultiplex packets into multiple RX queues based on destination MAC address and VLAN IDs
  Achieved by dedicating one RX queue to each guest

## Slide 28: Xen Network Design Changes

## Slide 29: Xen Network Design Changes
Guest copy move optimization remains useful
  Number of guests can exceed number of RX queues
  Still necessary for guest to guest traffic
  Packets from other guests contain copy grants

## Slide 30: Xen Network Design Changes
Multi-queue summary
  Device to guest data transfer reduces cost by 700 cycles
  Simplified socket buffer allocation and packet routing by 1150
  Grant mapping requires two grant copies (map and unmap) increasing cost by 650 cycles
Net reduction: 1200 cycles or 246% of native

## Slide 31: Xen Network Design Changes
Caching and reusing page grants
  Large percentage of Xen I/O CPU cycles due to page grants
  Memory isolation property slightly relaxed
  Driver domain keeps guest I/O buffers mapped in its address space
  Linux slab allocator caches previously used I/O buffers allowing page grants can be reused
  Security loss is minimal as DomD can only access I/O pages, no other data or code

## Slide 32: Xen Network Design Changes

## Slide 33: Xen Network Design Changes
Caching and reusing page grants
  Number of cached grants limited by address space of DomD kernel
  Grant reuse mechanism expected to have nearly 100% hit rate
  Amortized overhead should be nearly 0% over time
  Not yet implemented!
  Simplified, grant-free mechanism applied for simulation purposes
1950 cycles saved for total of 10,300 or 198% of native

## Slide 34: Xen Network Design Changes

## Slide 35: Tuning I/O Virtualization Configuration
Decoupling DomD from Dom0
  Xen allows DomD to be configured independently
  No fault isolation mechanism exists (e.g., detecting crashed drivers and restarting them)
  Hosting all device drivers in Dom0 limits flexibility
  e.g., Disabling bridge netfilter optimization cannot be applied or iptables does not work properly

## Slide 36: Tuning I/O Virtualization Configuration
Reducing interrupt rate
  Data copy and page grant overhead are proportional to traffic received
  Most remaining overhead proportional to number of times DomD and guest are scheduled
  Physical and virtual interrupts, events, hypercalls, etc.
  Device interrupt consumed by Dom0 and DomD, and the corresponding virtual interrupt in the guest

## Slide 37: Tuning I/O Virtualization Configuration
Reducing interrupt rate
  Modern NICs can delay interrupts until multiple packets received
  Interrupt rate can be controlled by driver parameters called interrupt coalescing parameters
  Interrupt generated when specified number of packets received or specified delay is reached
  Limits interrupts at high I/O rates but preserves latency at low rates
  Amortizes interrupt costs for Dom0, DomD, and guests

## Slide 38: Tuning I/O Virtualization Configuration

## Slide 39: Conclusion
Xen driver domain isolates device drivers from hypervisor and guest code
Device drivers need access to I/O data in guests and to move data between them resulting in overhead
Moving copy operations to guest CPU increases data locality
Data copies avoided by using HW to copy data directly into guest memory
Page grants can be reused by sharing I/O buffers
I/O tuning can greatly improve performance